## Slide 2: Mini-Bee
2PAX VTOL Hybrid Octocopter

## Slide 3: Agenda
Mini-Bee description
  Concept and technical description
  SWOT analysis
TRL1 project
  Partners and project history
  TRL1 Tasks
  Aerodynamic studies
TRL2 project launch
  (TRL2 = Technology concept and application formulated)
  Annexes : State of the art, Other innovative projects

## Slide 4: Mini-Bee : 2PAX VTOL Hybrid

## Slide 5: Mini-Bee description
Project state : beginning of TRL2
  Electric octocopter : 4 vertical + 4 tilt
  Hybrid energy : fuel + batteries
  2 seats, VIP configuration
Characteristics :
  VTOL capacity, short wings, 1.2 ton
  Range 600km, max speed 300km/h
  Electric controls and engines
Goals and market
  VIP, Air Ambulance, individual aircraft
  Estimated price 1m€ (for VIP)

## Slide 6: Architecture
Central vertical quadcopter
External tilt quadcopter
Gullwing doors
Biplane
Electric flight controls
Tailwheel-type landing gear
Retractable front landing gear
Fuel generators
Rear electric generator
Battery kits
3D printed metallic structure
Low noise nacelle

## Slide 7: Technical description
Aircraft characteristics
2 seats, VTOL, Short wing for cruise flight
MTOW 1200 kg, Range 800km , Cruise speed 220 km/h
Wing surface 15m², no control surface
Engines
Central vertical quadcopter + External tilt quadcopter
4 hybrid fuel generator for central quad copter
4 electric engines for external tilt quadcopter
Electronic control of engines power and tilt angles
Cockpit interface
« Car like » pilot interface : Steering wheel, foot pedals, central screen

## Slide 8: Take-off and flight transition
Vertical take-off
Tilt transition
Cruise flight
Supméca 2016
Estaca 2016

## Slide 9: Cruise flight

## Slide 10: Take-off and tilt transition
By Estaca 2016

## Slide 11: Technical data
MTOW : 1200 kg
Structure : 310kg
Fuselage : 80kg
Payload : 220 kg (2 PAX)
Systems : 125 kg
Engines : 240 kg (4 * generator + 8 Electric engines)
Batteries : 90kg
Fuel : 140kg
Target for TRL3 : MTOW 1000 kg

## Slide 12: Estimated costs
Total costs : 700k€
System : 200k€
Fuselage : 150k€
Wing : 100k€
Engines : 100k€
Landing gear : 50k€
Interior : 50k€
Other : 50k€

## Slide 13: Mission profile

## Slide 14: 8 Electric Engines
Equipement proposed : 8 electric
provided by
90kg of batteries during take-off and vertical flight
fuel generator during cruise flight
Hamza Fouatih 2016
Power needed 220 kW
Installed power 440kW
55k special designed engines (12kg/engine)
Or 8 engines Yuneec Power Drive 60

## Slide 15: 4 Electric fuel generator + Batteries
Equipement proposed : 4 Turbotech 55kW
Batteries : 1800 NCR 180650 in 10C (90kg)
Hamza Fouatih 2016

## Slide 16: SWOT analysis
Strengths
Opportunities
Threats
Weakness
VTOL capacities
Speed of an aircraft
Double quadcopter back-up in case of engine failure
Fuel energy range
New configuration
Project at low TRL
Aerodynamic and leight weight structure
Propulsion and energy storage
Project implementation
Project funding
All electric helicopter
All electric aircraft
Tilt rotor (bi and quadri)
Hybrid energy
Cost reduction :
  Overall flight cost reduction compared to helicopter
  Low purchasing & maintenance cost of engines
New design space: tilt, octocopter
  Weight / VTOL
Project investment

## Slide 17: Partners for R&D
TRL1 Basic Definition
Project coordinator
TRL2 Detailled Definition
In launch

## Slide 18: Project history
TRL0 Project Launch (2015)
TRL1 Basic Definition (2016)
Studies 2015/2016
TRL2 Concept (2016)
Lesser Open Bee License 1-3

## Slide 19: TRL1 project tasks
Polito 2015
Estaca
2016 group1
Supmeca & Polito
2016 (Placis)
Estaca
2016 group2
Supmeca
2016

## Slide 20: Aerodynamic studies
Cockpit shape optimization
Supmeca 2016
Rotor shape optimization
Supmeca 2016
Vertical rotor air flow studies
Supmeca 2016

## Slide 21: Mini-Bee project for TRL2
Mini-Bee (at end of TRL1)
2 PAX VIP
Electric Octocopter
Tilt quadcopter & vertical quadcopter
Hybrid energy : batteries & fuel
Estaca Laval 2016

## Slide 22: Overall main beeplane Project partners
Lesser Open Bee License 1-3
Coordinator :
Universities :
Design:
Institution & financial partners :

## Slide 23: Actions for Mini-Bee TRL2 Project
Launch Mini-Bee TRL2 project :
  Assess detailled technical configuration
  Evaluate market opportunities, production and flight costs
  Define partnership for TRL2 and TRL3
  Draw project financial path
  Investigate for lovemoney phase

## Slide 24: Partners to be defined
Aircraft manufacturer
Electronics and equipement integration
Cokpit interface and project integration
Aircraft flight management control
Project sponsors & finance
Structure metallic 3D printer
Luxury firm for VIP configuration
Air Ambulance end user
France
World
India
VIP end users
US

## Slide 25: Targeted Industrial Schem
Head quarters
Final Assembly Line for VIP config
Flight control system & Equipements
FAL for Standard Config & Air Ambulance
Engines
Metallic 3D printing
Testing, Customer service & Worldwide Logistic
IT Transport Management

## Slide 26: Financial project path
Estimated overall project 100m€

## Slide 27: Annexes
Individual Air Vehicules

## Slide 28: State of the art

## Slide 29: Other innovative projects
SoloTrek/Springtail
http://www.trekaero.com/
Airbus E-fan (all electric)
E-volo
eHang (fin 2015)
Xplorair (2016)
Airbus (2016)
Trifan 600 XTI aircraft
Boeing (2016)
Helium (2016)
Joby
Macro industrie (2016)
Moler skycar (2016)
Urban aeronautics (2016)
Lilium
zee.aero
+Kitty Hawk

## Slide 30: Mini-Bee
2PAX VIP Hybrid Octocopter