## Slide 2: Mini-Bee
2PAX VTOL Hybrid Octocopter

## Slide 3: Agenda : Mini-Bee TRL2 description
  TRL2 Partners
  Concept and technical description
  Cabine configurations
  Vehicule and system description
  SWOT analysis
  Project history
  Annexes :
  State of the art
  Other innovative projects

## Slide 4: Mini-Bee : 2PAX VTOL Hybrid

## Slide 5: Mini-Bee Project partners
Lesser Open Bee License 1-3
Coordinator :
Universities :
Design:
Institution & financial partners :

## Slide 6: Mini-Bee description
Project state : TRL2
  Electric octocopter : 4 vertical + 4 tilt
  Hybrid energy : fuel + batteries
  2-3 seats
Characteristics :
  VTOL capacity, short wings, 1.2 ton
  Range 600km, max speed 300km/h
  Electric controls and engines
Goals and market
  VIP, Taxi, Air Ambulance
  Estimated price 1m€ (0,7 to 2m€)

## Slide 7: Architecture
Central vertical quadcopter
External tilt quadcopter
Gullwing doors
Biplane
Electric flight controls
Tailwheel-type landing gear
Retractable front landing gear
Fuel generators
Rear electric generator
Battery kits
3D printed metallic structure
Low noise nacelle

## Slide 8: Technical description
Aircraft characteristics
2 to 3 seats, VTOL, Short wing for cruise flight
MTOW 1200 kg, Range 600km , Cruise speed 220 km/h
Wing surface 15m², no control surface
Engines
8 electric engines : Central vertical quadcopter + External tilt quadcopter
4 fuel generators + Batteries
Electronic control of engines power and tilt angles
Cockpit interface
« Car like » pilot interface : Steering wheel, foot pedals, central screen

## Slide 9: Take-off and flight transition
Vertical take-off
Tilt transition
Cruise flight
Supméca 2016
Estaca 2016

## Slide 10: Cruise flight

## Slide 11: Cabine configurations
1 PAX
2 PAX
3 PAX
Sport
VIP
Taxi
Ambulance
Utilities
4 PAX (light)

## Slide 12: VIP Configuration

## Slide 13: Architecture
Generators
Generators
Batteries
Batteries
Cockpit

## Slide 14: Modular structure
Delivery in 20’ Container
Production, delivery and MRO optimization
2 main flight configurations
Taxi :
VTOL Short intra city
Short wings, high NACA
Vertical central engines
Fixed landing gear
VIP :
VTOL + cruise
Longuer wings
Fuel capacities
Retractable landing gear
Estaca 2016

## Slide 15: Mission profile

## Slide 16: 8 Electric Engines
Equipement proposed : 8 electric engines 55k (50kg)
provided by
90kg of batteries during take-off and vertical flight
4 fuel generators during cruise flight
Power needed 220 kW
Installed power 440kW
55kW special designed engines (12kg/engine)
Or 8 engines Yuneec Power Drive 60kW

## Slide 17: 4 Electric fuel generator + Batteries
Equipement proposed : 4 Turbotech 55kW (160kg)
Batteries : 1800 NCR 180650 in 10C (90kg)

## Slide 18: Data
MTOW : 1200 kg
Structure : 310kg
Fuselage : 80kg
Payload : 220 kg (2 PAX)
Systems : 125 kg
Engines : 240 kg
Batteries : 90kg
Fuel : 140kg
Target for TRL3 : MTOW 1000 kg
Total costs : 700k€
System : 200k€
Fuselage : 150k€
Wing : 100k€
Engines : 100k€
Landing gear : 50k€
Interior : 50k€
Other : 50k€
Target for standard configuration : Price = 700k€

## Slide 19: SWOT analysis
Strengths
Opportunities
Threats
Weakness
VTOL capacities
Speed of an aircraft
Double quadcopter back-up in case of engine failure
Fuel energy range
Aircraft Design and configuration
Lesser open source collaborative project
New configuration
Project at low TRL
Aerodynamic and leight weight structure
Propulsion and energy storage
Project implementation
Project funding
All electric helicopters and VTOL vehicules
All electric aircrafts
Drones
Tilt rotor
Hybrid energy
Others innovative projects
Cost reduction :
  Overall flight cost reduction compared to helicopter
  Low purchasing & maintenance cost of engines
New design space: tilt, octocopter
  Weight / VTOL
Project investment

## Slide 20: Partners for R&D
TRL1 Basic Definition
Project coordinator
TRL2 Detailled Definition
In process
Lesser Open Bee License 1-3

## Slide 21: Project history
TRL0 Project Launch (2015)
TRL1 Basic Definition (2016)
Studies 2015/2016
TRL2 Concept (2016) in Process
Lesser Open Bee License 1-3
Meet us in
Le Bourget Air Show 2017 !
2016/2017

## Slide 22: Aerodynamic studies
Cockpit shape optimization
Supmeca 2016
Rotor shape optimization
Supmeca 2016
Vertical rotor air flow studies
Supmeca 2016
Numerical studies
Supmeca, end of 2016

## Slide 23: Actions for Mini-Bee TRL2 Project
Mini-Bee TRL2 tasks :
  Refine detailled technical and equipement configuration
  Evaluate market opportunities, production and flight costs
  Define partnership for TRL2 and TRL3
  Draw project financial path
  Investigate for lovemoney phase

## Slide 24: Partners to be defined
Aircraft manufacturer
Electronics and equipement integration
Cokpit interface and project integration
Aircraft flight management control
Project sponsors & finance
Structure metallic 3D printer
Luxury firm for VIP configuration
Air Ambulance end user
France
World
Asia
VIP end users
US

## Slide 25: Targeted Industrial Schem
Head quarters
Final Assembly Line for VIP config
Flight control system & Equipements
FAL for Standard Config & Air Ambulance
Engines
Metallic 3D printing
Testing, Customer service & Worldwide Logistic
IT Transport Management and project funding
India
US
Normandy
Europe

## Slide 26: Financial project path
Estimated overall project 100m€
Actual step : Lovemoney for 500k€ to 2m€
First flight
Test flights
Commercialisation / Operations
Final developments
Qualification
Detailled numerical mock-up

## Slide 27: Uber Elevate planning

## Slide 28: Annexes
Individual Air Vehicules

## Slide 29: Mini-Bee project for TRL2
Mini-Bee (at end of TRL1)
2 PAX VIP
Electric Octocopter
Tilt quadcopter & vertical quadcopter
Hybrid energy : batteries & fuel
Estaca Laval 2016
Lesser Open Bee License 1-3

## Slide 30: Take-off and tilt transition
By Estaca 2016

## Slide 31: TRL1 project tasks (2015/2016)
Polito 2015
Estaca
2016 group1
Supmeca & Polito
2016 (Placis)
Estaca
2016 group2
Supmeca
2016

## Slide 32: State of the art
X3 airbus
Osprey V22
Airbus H160
Ecureuil
X2

## Slide 33: Other innovative projects
SoloTrek Springtail
Trekaero.com
Airbus E-fan (2015)
E-volo (<2014)
eHang (fin 2015)
Xplorair (2016)
Airbus (2016)
Trifan 600 XTI (2015)
Boeing (2016)
Helium (2016)
Joby (2016) ~ 100m€
Macro industrie (2016)
Moler skycar (<2016)
Urban aeronautics
(<2016)
Lilium (2016) ~10m€
zee.aero (2016)
Kitty Hawk (2016)
Mini-Bee (2016)
Agusta Westland
Zero (2015)
Airbus Vahana (2016)
Olympus (2016)

## Slide 34: Mini-Bee
2 PAX VIP Hybrid Octocopter
Lesser Open Bee License 1-3